## Slide 1: By Yerramsetti Chaitanya Kumar 22m1164
Dual clock FIFO

## Slide 2: FIFO is like a queue:
FILLED
FILLED
FILLED
FILLED
FILLED
7
6
5
4
3
2
1
0
WP
RP
Next Empty Slot
in the queue.
(Tail of the queue)
Similar to WP
Senior-most person in
the queue
(Head of the queue)
Similar
to RP

## Slide 3: FIFO PIN-OUT
CLK
WD (WRITE DATA)
RD (READ DATA)
FIFO
WEN
Write Enable (from the Producer)
REN
Read Enable (from the Consumer)
FULL
Full status info (to the Producer)
EMPTY
Empty status (to the Consumer)
AF (ALMOST FULL)
AF status info (to the Producer)
(Optional)
AE (ALMOST EMPTY)
AE status info (to the Consumer)
(Optional)

## Slide 4: FIFO Block Diagram
WD (WRITE DATA)
RD (READ DATA)
FIFO
WEN
Write Enable (from the Producer)
REN
Read Enable (from the Consumer)
FULL
Full status info (to the Producer)
EMPTY
Empty status (to the Consumer)
AF (ALMOST FULL)
AF status info (to the Producer)
(Optional)
AE (ALMOST EMPTY)
AE status info (to the Consumer)
(Optional)
WP
RP
Wr_CLK
Rd_CLK

## Slide 5: Producer
Producer
Consumer
FIFO
Producer
Consumer
1-location Buffer
Consumer

## Slide 6: FIFO
PRODUCER
Writer
Deposits Data into the FIFO.
CONSUMER
Reader
Reads Data from the FIFO.
Delinks the producer and the
consumer

## Slide 7: Let us use an 8-location FIFO for our design example
PRODUCER
CONSUMER
7
6
5
4
3
2
1
0
WP RP
Initially
The FIFO has two pointers to denote the locations to write and read:
  Write Pointer (WP): The location pointed to by the WP is where producer deposits data.
  Read Pointer (RP): The location pointed to by the RP is from where consumer reads data.
Initially the FIFO is empty. Both WP and RP point to location 0 of the FIFO.

## Slide 8: Points to the location to be written
PRODUCER
CONSUMER
FILLED
FILLED
FILLED
FILLED
7
6
5
4
3
2
1
0
WP
RP
Points to the location
to be read

## Slide 9
PRODUCER
CONSUMER
FILLED
FILLED
FILLED
FILLED
FILLED
7
6
5
4
3
2
1
0
WP
RP
Now if we write to location 7, should the WP be incremented and be allowed to point to location 0?

## Slide 10: FIFO Storage Register Array acting as a Dual Port Memory
RA2 RA1 RA0
WEN
REN
WD3 WD2 WD1 WD0
RD3 RD2 RD1 RD0
WA2
WA1
WA0
RA2
RA1
RA0
WD3
WD0
WD1
WD2
RD3
RD0
RD1
RD2
WENQ
RENQ
CLK
WA2
DUAL PORT RAM
WA1 MEMORY
WA0
8x4
WA
RA
WD
RD
(a write-only (WO) port and a read-only (RO) port)

## Slide 11: WP and RP pointers – when to increment them
WP RP
FULL
WEN
EN
WA2
WA1
WA0
QA
QB QC
CLK
CLK
CLR~
RESET~
WENQ
WP
EMPTY
REN
RA2
RA1
RA0
QA
QB QC
RESET~
RENQ
RP
CLK
CLR~
CLK
EN

## Slide 12: For SEQUENTIALLY changing data such as WP and RP use GRAY CODE
WP
WPS
Gray
Counter
Since only 1-bit changes at most in WP, the WPSS will
either be the old WP or the new WP and
will never
be an absurd value!
0 | 0 | 0
 |  | 1
 | 1 | 1
 |  | 0
1 | 1 | 0
 |  | 1
 | 0 | 1
 |  | 0
GRAY CODE:

## Slide 13: Say FWCLK >> FRCLK
7
6
5
4
3
2
1
0
WP
RP
EMPTY= 1
ALMOST_EMPTY= 1
Consider the junior engineer’s
design with AE and AF.
AE==1 when (WP-RP)mod8 = 2
AF==1 when (WP-RP)mod8 = 6
FULL= 0
ALMOST_FULL= 0
FIFO is initially empty.
So FULL=0 and ALMOST_FULL=0;
EMPTY=1 and ALMOST_EMPTY=1
RCLK
WCLK

## Slide 14: RCLK
7
6
5
4
3
2
1
0
WP
RP
WCLK
EMPTY= 1
ALMOST_EMPTY= 1
FULL= 0
ALMOST_FULL= 0
Suppose the producer starts writing the data after the 1st clock edge of WCLK for 8 consecutive clocks.

## Slide 15
FILLED
7
6
5
4
3
2
1
0
WP
RP
RCLK
WCLK
EMPTY= 1
ALMOST_EMPTY= 1
FULL= 0
ALMOST_FULL= 0

## Slide 16
FILLED
FILLED
FILLED
7
6
5
4
3
2
1
0
RP
RCLK
WCLK
ALMOST_FULL= 0 WP
EMPTY= 1
ALMOST_EMPTY= 1
FULL= 0

## Slide 17
FILLED
FILLED
FILLED
FILLED
FILLED
7
6
5
4
3
2
1
0
WP
RP
RCLK
WCLK
EMPTY= 1
ALMOST_EMPTY= 1
FULL= 0
ALMOST_FULL= 0

## Slide 18
FILLED
FILLED
FILLED
FILLED
FILLED
FILLED
FILLED
7
6
5
4
3
2
1
0
WP
RP
RCLK
WCLK
EMPTY= 1
ALMOST_EMPTY= 1
FULL= 0
ALMOST_FULL= 1

## Slide 19
FILLED
FILLED
FILLED
FILLED
FILLED
FILLED
FILLED
FILLED
7
6
5
4
3
2
1
0
WP
RP
RCLK
WCLK
EMPTY= 1
ALMOST_EMPTY= 1
FULL= 1
ALMOST_FULL= 1
FIFO becomes full.

## Slide 20
RESULTS

## Slide 21
RESULTS

## Slide 22
RESULTS

## Slide 23
Thank you